## Slide 1: Computer Architecture W3D2: Modeling and Implementation
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Roadmap
What is modeling?
What is implementation?
What is the gap b/t?

## Slide 3: A Typical Architecture Design & Impl. Process
I don’t want to waste my engineering effort.
I have a good architecture idea!
HARDware implementation is too HARD
A problem is solved by introducing another
  Separate implementation, separate teams

## Slide 4: Characterizing the Modeling Methods
Analytical Model
Functional Sim.
RTL Simulation
Verilator
Gate-level
Higher-level Performance Estimation
More low-level insights
Lower Impl Difficulties
Higher Impl Difficulties
Shorter time to estimate
Longer time to simulate

## Slide 5: Characterizing the Modeling Methods
Functional Simulation
  Execution-based: Simulate binary executable
  Feed the binaries to a simulator simulates what the hardware does
add t1, t2, t3
sub t3, t1, t2

## Slide 6: Characterizing the Modeling Methods
Functional Simulation
  Trace-based: Instrument before every inst.
  Execute the raw program to generate the trace
  Simulate the traces
# before instrument
add t1, t2, t3
sub t3, t1, t2
# before instrument
print "add t1 t2 t3"
add t1, t2, t3
print "sub t3, t1, t2"
sub t3, t1, t2

## Slide 10: Sw/hw Co-designs
Performance: Cycle-Accurate Simulator
Power/Area: RTL Synthesis
Alignment: Who cares?
Chart: Evaluation Methodology
| Pure Software | RTL Simulation | Simulator+RTL Synthesis | Simulator Only
比例 | 0.08 | 0.2 | 0.48 | 0.24
Chart: 
| ISCA-2023 | ISCA-2024 | HPCA-2024
Accel+uArch | 25 | 30 | 25
Other | 58 | 57 | 60

## Slide 11: Insights and Principles
Ideal Solution: A unified and easy programming interface for both simulation & implementation
IF
IF
ID
IF
ID
EX
Cycle 1
Cycle 2
Cycle 3
……
def engine():
while !q.empty():
e = q.front()
e.sim(q)
class IF():
def sim(q: Queue):
inst = icache[self.pc]
q.enqueue(ID(inst))
class ID():
def sim(q: Queue):
opcode,a,b =
decode(self.inst)
q.enqueue(EX(opcode,a,b))
Simulation Trace:
IF
ID
EX
MA
WB
Unified: Some commonality b/t sim and impl.
Easy: Better behavior-oriented abstraction
Notes: I think a very first insight I would like to emphasize is that application domain does not necessarily define a domain-specific accelerator. Application behaviors of interests do, and herein will be referred as computing idioms.
If we would like to have a design automation, we first need a well-defined design space. The principle of having such a design space is that many hardware specialization mechanisms can be approximated by composing a set of simple and common primitives, and all these mechanisms can be modularly integrated to a target hardware.
Though we are automating domain-specific accelerator design, the domain itself is agnostic. Therefore, the universal space of accelerator design should be general purpose, while getting rid of the VN overheads. In this case, we adopt the decoupled-spatial paradigm.

## Slide 12: Insights and Principles (CONT’D)
What if I rearrange it a little bit?
IF
IF
ID
IF
ID
EX
Cycle 1
Cycle 2
Cycle 3
……
Simulation Trace:
RTL Waveform:
In principle, we can have a 1-1 correspondence
But we don’t achieve it for many reasons [1]…
[1] https://research.cs.wisc.edu/vertical/papers/2014/wddd-sim-harmful.pdf
Notes: I think a very first insight I would like to emphasize is that application domain does not necessarily define a domain-specific accelerator. Application behaviors of interests do, and herein will be referred as computing idioms.
If we would like to have a design automation, we first need a well-defined design space. The principle of having such a design space is that many hardware specialization mechanisms can be approximated by composing a set of simple and common primitives, and all these mechanisms can be modularly integrated to a target hardware.
Though we are automating domain-specific accelerator design, the domain itself is agnostic. Therefore, the universal space of accelerator design should be general purpose, while getting rid of the VN overheads. In this case, we adopt the decoupled-spatial paradigm.

## Slide 13: Why is RTL implementation hard?
Or, why simulation is easier?
  😭 C++ does not enforce you only write a reg once a cycle
  😠 vector<T>::push_back does not enforce your buffer size
  🤔 Some data structure manipulation/state machine is too hard
These are part of the problem.
  Execution model

## Slide 14: Write every register only once!
Each register can only be written once every cycle
 Manually gather all the sources of deltas
 Concurrency are fake!
// In C++
// Site 1.
if (cond0) { reg++; }
// Site 2.
if (cond1) { reg--; }
// In Verilog
delta0 = cond ? 1 : 0;
delta1 = cond ? 1 : 0;
reg <= reg + delta0 – delta1;

## Slide 15: Buffer Overwhelming
Even a simple code can construct a super long chain of RAW.
What is wrong with this?
😠 In simulator, you can simply do
😭 In RTL, you will overwhelm the inter-stage register
// In C
b[a[i]]++;
# r2 is i
load r1, a(r2)
shli r1, r1, 4
load r3, b(r1)
addi r3, r3, 1
sw r3, b(r1)
id.push_back(inst)

## Slide 16: Diverged: Initial Interval
Initial Interval: The interval b/t two launches of execution
II=1: Fully pipelined, the ideal performance
What is the II here?
Question: Can we have a 500-stage pipeline?
// In C
b[a[i]]++;
# r2 is i
load r1, a(r2)
shli r1, r1, 4
load r3, b(r1)
addi r3, r3, 1
sw r3, b(r1)

## Slide 17: Data Structure Manipulation
Find an instruction that can be issued for execution in reservation station
foreach reservation station {
if rs1.valid && rs2.valid {
issue for execution }
}

## Slide 18: Why is RTL implementation hard? (CONT’D)
Or, why simulation is easier?
  😭 C++ does not enforce you only write a reg once a cycle
  😠 vector<T>::push_back does not enforce your buffer size
  🤔 Some data structure manipulation/state machine is too hard
These are part of the problem.
  A Gap of Execution model

## Slide 19: How pipelined architectures are taught?
A stage finishes its duty and pushes remaining jobs to the next ones
IF: “I read the manual for instructions!”
ID: “I check the data availability!”
EX: “I do the computation!”
MA: “I am the warehouse keeper!”
WB: “I check in the results!”

## Slide 20: Asynchronized Event Handling
Decode my fetched instruction, please.
OK. I promise it will be decoded, but not now
Why this happens?
  A too long critical path may hurt the timing
What do we need?
  A clear boundary between the “current” and “next” cycle
IF
ID
What is async?
x = async foo(1, 2) // A Promise returned
x.when(function (result) {
// use the returned value here.
})
foo will be done, but not immediately;
a promise is returned to use the result when ready

## Slide 21: What is “async” function call?
What is sync?
What is async?
function foo(a, b) {
// do something here
}
foo(1, 2) // a sync call
When calling foo, the program counter immediately move to foo: tag.
x = async foo(1, 2) // A Promise returned
x.when(function (result) {
// use the returned value here.
})
foo will be done, but not immediately;
a promise is returned to use the result when ready

## Slide 22: How are pipelined architectures implemented?
Every stage listens to the valid signal
When enabled acts its functionality
Remember this!
Will be explained later!
# Instruction Decoder
if inst.valid {
inst.pop_valid = true
opcode, operand = decode(inst)
if all operands available {
if EX resource available {
EX.push_valid = true
EX.data1 = rs1
EX.data2 = rs2
# ...
} }
}

## Slide 23: Mis-alignment: Push? Pull?
Architectural design
  OK. I finished my job this stage, and I push it to the next.
Architectural implementation
  Carefully listen to my related signal. When enabled pull the data in.
Let me further make an example in algorithm implementation

## Slide 24: How do you do a shortest path on DAG?
Push?

## Slide 25: How do you do a shortest path on DAG?
Pull?

## Slide 26: How do you do a shortest path on DAG?
They are anyways Turing-equivalent, which suggests a possible conversion

## Slide 27: How are pipelined architectures implemented?
RTL: Register-level Transfer
Every stage listens to the valid signal
When enabled acts its functionality
# Instruction Decoder
if inst.valid {
inst.pop_valid = true
opcode, operand = decode(inst)
if all operands available {
if EX resource available {
EX.push_valid = true
EX.data1 = rs1
EX.data2 = rs2
# ...
} }
}

## Slide 28: An Analogy: Event-listening
Did you write anything w/ UI before?
How is it implemented?
  The browser arranges something like a thread (co-routine) listens to this button
  Once clicked the PC will jump to functionToExecute()
<element onclick="functionToExecute()"> Click </element>

## Slide 29: Event-listening (CONT’D)
Did you write anything w/ UI before?
What is something like a thread, but not a thread?
  Let’s look at an example (of a bad demo of web frontend development)
<element onclick="functionToExecute()"> Click </element>

## Slide 30: Why? What is a co-routine then?
Do you have a driver’s lic?
Did you use yield in Python?
Returned, but not fully returned.

## Slide 31: Yielded Co-routine (CONT’D)
“Returned, but not fully returned”
Decode my fetched instruction, please.
OK. I promise it will be decoded, but not now
IF
ID

## Slide 32: Yielded Co-routine (CONT’D)
“Returned, but not fully returned”
Yield: ID stopped execution, but not finished
Return: ID finished execution, and ready for the next
OK. I am backlogged. I should pause now.
Sorry. I am decoding, but data is not available
IF
ID

## Slide 33: Summary
A gap between design and implementation
  Design: Pushed
  Impl: Pulled
A opportunity of Turing Equivalence
  Push and pull are doing exactly the same thing

## Slide 34: Assassyn: A Unified Abstraction for both Simulation and Synthesis
The Asynchronicity: Something will for sure happen but not know
What is asynchronized?
  The state, the side effect.
Decode my fetched instruction, please.
OK. I promise it will be decoded, but not now
IF
ID

## Slide 35: Assassyn: A Unified Abstraction for both Simulation and Synthesis
Source: https://github.com/Synthesys-Lab/assassyn
Set everything up
  I strongly recommend not to use M-series MacBook 🤦🏻‍♀️
  Use Docker to setup the environment dependencies
docker build -t assassyn:latest .

## Slide 36: Assassyn: Getting Started.
And then mount the repo to execute
docker run --rm -tid -v `pwd`:/app \
--user root \
--name assassyn \
assassyn:latest
Image
Name of the container
Mount the folder
Physical Machine
VM
Repo

## Slide 37: Assassyn: Getting Started.
Attach to this docker container
docker attach assassyn # attach to shell
$ <in side the container>
$ <C-p><C-q> # detach the container w/o exiting

## Slide 38: Assassyn: Getting Started.
Attach to this docker container
Self-exemplified code development
docker attach assassyn # attach to shell
$ <in side the container>
$ cd python/unit-tests/
$ python unit-tests/test_async_call.py

## Slide 39: A Simple Example: 2-Stage Pipeline
Driver stage
  Self-increases cnt every cycle
  Pushes cnt to Adder stage
Adder
  Adds up value from Driver
Driver
Adder
++cnt

## Slide 40: 2-Stage Pipeline (CONT’D)
Driver stage
  Driver invokes adder async-ly
Adder
  Processes driver’s data from last cycle
Driver
Adder
++cnt

## Slide 41: Understanding Each Stage
The logic of each stage: Adder

## Slide 42: Understanding Each Stage (CONT’D)
The logic of each stage: Driver

## Slide 43: Understanding Each Stage
Sequential logic is not committed until next cycle.

## Slide 44: Understanding the DSL
Trace-based DSL
Did you know what is operator overloading?
Did you know that operator overloading can be used to build DSL frontend?

## Slide 45: Trace-based DSL Implementation
Did you know how to overload a function in Python?
  __xx__
Did you know with in Python?

## Slide 46: Therefore, it is wrong to do this…
You cannot overload = in Python
You can only overload a[b] = c in python

## Slide 47: Understanding the Top Function
sys is the data structure of AST
with sets sys to the current AST
Every move within the recursively called function will be appended to the AST

## Slide 48: Understanding the Top Function (CONT’D)
Decoupled interface and implementation
Function signature of each function is fixed
build is a function implements function

## Slide 49: Elaborate the System
Elaborator traverses the AST for codegen
Simulator in Rust
RTL implementation in PyCDE
  A Python-ized Verilog Generator

## Slide 50: Code Generation: Simulator
A Cycle is separated into 2 halves
  1st Half: Executing the Combinational Logic Functions
  2nd Half: Commit the side effect registers
IF
IF
ID
IF
ID
EX
Cycle 1
Cycle 2
Cycle 3
……
Combinational Logic
Sequential Logic

## Slide 51: Code Generation: Simulator Runtime (CONT’D)
IF
IF
ID
IF
ID
EX
Cycle 1
Cycle 2
Cycle 3
……
Simulate Funcs
Commit Regs
class Fetcher:
@constructor
def __init__(self):
self.pc = Reg(int32)
@combinational
def build(self, decoder, inst_buffer):
inst = inst_buffer[self.pc]
decoder.async_call(inst)
self.pc += 4
# 1st-half
tmp = self.pc + 4
self.pc.write(tmp)
# 2nd-half
self.pc.commit()
Within cycle x, pc is not updated until the 2nd half of this cycle.
Rest of the combinational logic will still see self.pc rather than self.pc + 4
Bookkeep a pending write in runtime
Commit the result in runtime
Essentially, this is the SAME as Verilog simulation, but it determines the active regions in a coarser-grain way. Thus speedup is achieved (see eval later).

## Slide 52: Before Hardware: Valid-Ready Protocol
Valid: Data is valid to use
Ready: The downstream is ready to accept data
Upstream
Downstream
Ready
Valid
Data

## Slide 53: RTL Generation: Micro-architectural Support
Each function is a pipeline stage
Implicitly,
  All the stage registers are FIFOs
  A Counter SM is imposed to bookkeep executions
Counter State Machine
  Each function call increases
  Each execution decreases
  Counter != 0 enables stage execution

## Slide 54: Micro-architectural Support (CONT’D)
Counter, Register and FIFO adopt a “gather and write” paradigm
  A key difference is that counter uses “+” to gather, while other 2 use “|”
Registers are independent from each stage
FIFO will fall back to registers when depth=1