## Slide 1: Computer Architecture W6D2: Multithreading (Happy Summer Break🤦🏻‍♀️)
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Roadmap
Multi-threading
  Why?
  How?
GPU: A super multi-threading

## Slide 3: Why do we need multiple threads?
Parallelism? (//-ism)
  Part of the story (More on this later)
  Parallelism for what?
  What is the granularity of parallelism?
Fine-grain: Instruction-level //-ism
Fine-grain: Data //-ism SIMD
Coarse-grain: Thread //-ism
?: Memory //-ism

## Slide 4: Parallelism for what?
Performance and Utilization
Multi-issue has idles
  4-way is typically 1.5-2 → Less than 50% utilization
  Cache misses
  Data depdences

## Slide 5: Underutilization
Vertical waste
The whole pipeline not issued
Long latency dependences
  Division?
  Cache miss

## Slide 6: Underutilization
Horizontal waste
Some of the issue width not util.
Fine-grain dependences
  Data hazard? Especially RAW.
What should we do?
  Borrow something do-able!

## Slide 7: Fine-grain Solution: Software Pipelining
Why we are bad?
  Dependences among instructions
What do we observe?
  No dependences across the iterations
👉🏻 Borrow independent instructions from next iterations
// Original C Code
for (i=0; i<n; ++i)
c[i] += a[i] * b[i];
// A simple optimization
for (i=0; i<n; i += 2) {
c[i+0] += a[i+0] * b[i+0];
c[i+1] += a[i+1] * b[i+1]; }

## Slide 8: Fine-grain Solution: Software Pipelining
Borrow independent instructions from next iterations
// A simple optimization
for (i=0; i<n; i += 2) {
c[i+0] += a[i+0] * b[i+0];
c[i+1] += a[i+1] * b[i+1]; }
loop:
load a[i+0], rs1
load b[i+0], rs2
load c[i+0], rs3
mul rs4, rs1, rs2
load a[i+1], rs1
add rs5, rs4, rs3
load b[i+1], rs2
store rs5, c[i+0]
load c[i+1], rs3
mul rs4, rs1, rs2
add rs5, rs3, rs4
# increase by 2
# loop back
Ooops? We are screwed again?

## Slide 9: How many iterations should we unroll?
Revisit the data dependence graph
Fill the bubbles with borrowed instructions
×
＋
A
B
C
D
×
＋
A
B
C
D





(a) Data Dependence Graph
(b) Serialize the execution
×
＋
A
B
C
D
×
＋
A
B
C
D
(c) Borrow instructions

## Slide 10: How many iterations should we unroll?
Fill the bubbles with borrowed instructions
Theoretically, we can unroll more to get better performances
×
＋
A
B
C
D
×
＋
A
B
C
D
Borrow instructions
If not unrolled, we have 2 bubbles per iteration
  Each iteration is 7-instruction
If unrolled by 2, we still have 2 bubbles per iteration
  Each iteration is 13-instruction
Can we unroll infinitely?
  Register pressure
  Binary size
Sol: Cross-iteration execution schedule

## Slide 11: How many iterations should we unroll?
Sol: Cross-iteration execution schedule
  Borrow ‘store’ from the prior iteration
  Initialize the value computation outside
  Cleanup the last one
×
＋
A
B
C
D



Initialize the first loop
Cleanup the last result

## Slide 12: Wait! Let’s revisit the data dependence graph.
The last solution is a little bit ad-hoc
Do we have a formalized paradigm?
  Execute across 4 iterations
Wait! How could we encode this?
×
＋
A
B
C
D
1
2
3
4
loop:
bring a[i] to reg1
bring b[i] to reg2
reg1 = reg1 * reg2
bring c[i] to reg3
reg3 = reg3 + reg1
send reg3 to c[i]
increase i by 1
go back to loop when i<n
Challenge: New data in this iteration may overwrite the old one before usage.

## Slide 13: Intel Itanium
Dependent Instructions
  Dynamic Register Indices
  r_{i,j,k}
×
＋
A
B
C
D
1
2
3
4
# load for this iteration
load a[i], r{0,1}
load b[i], r{2,3}
load c[i], r{4,5}
# compute for last iteration
r{6,7} = mul r{1,0}, {3,2}
r{8,9} = add r{6,7}, c{5,4}
store {9,8}
Is the instruction order scheduling simplified because of more flexible borrow?

## Slide 14: Intel Itanium (CONT’D)
Independent Instructions
  VLIW Very Long Instruction Word
  E.g. pack A, B, C into one slot.
×
＋
A
B
C
D
1
2
3
4
# load for this iteration
{
load a[i], r{0,1}
load b[i], r{2,3}
load c[i], r{4,5}
}
No, register ration x instruction packing makes the whole thing exponentially more complicated 😭

## Slide 15: Multi-threading: An Intuitive Glance
This is a coarse-grain solution
Thread A: executes 10s for latency
Thread B: executes 20s for latency
Sequential execution: 10+20 = 30
Executes A and B together: Maybe 25s?
  Fine, A is +15s slower (questionable)
  B is (for sure) +5s slower
  Improves -5s for executing both

## Slide 16: Get back to these example
When thread A is idle
Can we use those un-used units for better performance?
Yes, but needs more support
  What should we retain across different threads?

## Slide 17: Goal: Execute across A & B
Borrow Thread B’s instruction to fill the execution pipeline
When A is idle for memory latency, B’s execution hides A’s idle
What additional support we need for this?

## Slide 18: Implementing Multi-threading
IF: PC register
  Duplicated: A.PC & B.PC
ALU
  Not stateful
  Shared
Soft states
  Cache, BP?: Talked before
Registers
  Logic registers
  RS, ROB, and other bookkeeping

## Slide 19: Implementing Multi-threading
Main Question
  When to execute another thread?
Derived Question
  How to manage thread states?
Key tradeoff
  What kind of performance to achieve?
  What kind of cost to pay?
Three designs
  CG, FG, and SMT

## Slide 20: Coarse Grain MT
Explicitly switch across threads
IF
ID
EX
MA
WB
IF
ID
EX
MA
WB
Before:
After:
Scheduler
B.RF
A.RF

## Slide 21: Coarse Grain MT (CONT’D)
L2 | Mis |  | 
Switch across threads by scheduler
Scheduler arbitrates which to exec.
  On L2 miss
Stateful partitioned
  Register file
  ROB
  BP
No worse than 1 thread
Easy to impl.
IF
ID
EX
MA
WB
Scheduler
B.RF
A.RF

## Slide 22: Fine Grain MT
Switches thread every cycle
  No matter L2 miss
Pipeline threading states partitioned
  As the same before
Tradeoffs
   Simple
   Tolerates high latency
   Significantly sacrifices single thread perf.
   Needs a lot of threads
GPU adopts this strategy!

## Slide 23: Fine-Grain MT (CONT’D)
Round-robin Scheduling
Long in short: Take turns to execute
Trivial Solution:
  grant = (grant + 1) % N
  What if we have un-ready?
Grant to the “next ready” one
IF
ID
EX
MA
WB
RR Sched.
B.RF
A.RF

## Slide 24: Round-robin Scheduler
Trivial Solution
  grant = (grant + 1) % N
A more aggressive solution
  Grant to “next ready” one
Assuming ready is the ready bit-vector
  Next half: ready & ~(1 << last_grant)
  First half: ready & ((1 << last_grant) - 1)
  Select low bit of next half first higher than first half

## Slide 25: SMT: Simultaneous MT
Finer than fine-grain scheduling
Thread executions are mixed
Aggressively issue all insts with valid operands across threads
Scheduling? Resource partitioning?
Example: Pentium 4 Hyperthreading
  4 core, 8 thread

## Slide 26: SMT Implementation
Wait, how can I deal with sooo many register partitions without an explicit boundary threads?
Recap: What did we do for OoO?

## Slide 27: Too many data movements
ROB to Reg
TMap to RS
ROB/Reg to Operand Buffer
ID
IF
C
R
RS
Allocate on ROB
ROB
TMap
Check/update data validity
Writes result
Reg
Commit result
EX
Bookkeeping
Logics

## Slide 28: Alternative: MIPS R10K
Big Idea: Use a big physical register file to hold all data without copies
   Registers are only for FUs
   ROB is just a side data structure for reordering

## Slide 29: Alternative: MIPS R10K (CONT’D)
Architecture logic registers are fully gone, just like other register renamings
Fundamental Change: TMap
  Instead of having a cyclic FIFO for ROB-based register renaming, a free list is maintained to allocate registers
  ROB commitment frees allocated register

## Slide 30: Key Challenge: Maintaining Renaming
Consider the example right
We have logic register r1-3
Physical register p1-7
  Initially, p1-3 maps to r1-3
Key question
  When to free the allocated physical register?
  Wrong Answer: Free it upon retirement.
  No register copy to it!
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3

## Slide 31: Register Renamed OoO
A super big centralized register file managed by renam-ing
ID
IF
C
R
RS
Allocate on ROB
ROB
RegN
Check/update data validity
Writes result
Physical Register File
Commit result
EX
Bookkeeping
Logics

## Slide 32: SMT uses Register Renaming
Pooling the register resources
Partition isolation done by renaming
ID
IF
C
R
RS
Allocate on ROB
ROB
RegN
Check/update data validity
Writes result
Physical Register File
Commit result
EX
Bookkeeping
Logics
Sched
RegN
RegN

## Slide 33: Summary
OoO is naturally a good fit SMT
  Issue logic did not even changed!
  Renaming logic is simply duplicated!
Thanks to Moore’s Law
  More transistors, more registers, and more logics for more aggressive designs
  #map-table = #threads * #logic-reg
  #phy-reg = #threads * #logic-reg + #in-flight-insts

## Slide 34: Other resources? LQ/SQ?
How are LSQs shared?
Dedicated or pooling?
N slots in LSQ, N/T entries each thread
   Simple! Isolate high/low ILP insts
   Low utilization sometimes
Dynamically shared
  Allocation by thread tagging?
  Non-memory-intensive ones may be stalled memory-intensive ones.

## Slide 35: Other resources? BP?
Challenges
  Sharing global states across many threads
  Predict multiple threads together
Good
  Less need for branch prediction?
  Speculate less far in each thread
  We have more borrowed parallelism already!

## Slide 36: Helper thread for X?
Prefetching
Branching
Idea: Run a light-weighted pruned thread ahead to know the result early
Use the result to guide main execution
Fork
Pred
BR
Load
Speedup

## Slide 37: Summary
Multi-threading
  Coarse-grain parallelism is just part of the story
  Threads hides the latency by filling in the idle pipeline
  A part of transistor scaling, use unused resources

## Slide 38: Motivation
Compute is fast!
Look at this CPU, whose clock rate is 4.3GHz
An addition can be done within ~0.23ns

## Slide 39: Roadmap
Multi-threading
  Why?
  How?
GPU: A super multi-threading