## Slide 1: Computer Architecture W4D1: A Deeper Tour to Assassyn
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Resources
All the code demo are available at
  https://github.com/were/sys-arch
  TODO: Better documentation
  TODO: Add a better .gitignore

## Slide 3: Roadmap
Recap: A simplest 2-stage pipeline
Do we really understand every line?

## Slide 4: Recap: 2-Stage Pipeline
Driver stage
  Self-increases cnt every cycle
  Pushes cnt to Adder stage
Adder
  Adds up value from Driver
Driver
Adder
++cnt

## Slide 5: Recap: Understanding Each Stage
The logic of each stage: Adder

## Slide 6: Understanding Each Stage (CONT’D)
The logic of each stage: Driver

## Slide 7: Roadmap
Recap: A simplest 2-stage pipeline
Do we really understand every line?
  Decorator
  Partial

## Slide 8: Recap: Trace-based DSL
Execute the code to grow the AST
AST appended to its corresponding AST node
What happened behind the frontend?

## Slide 9: Recap: Trace-based DSL (CONT’D)
Create IR node in __add__
Append it to AST

## Slide 10: Recap: Trace-based DSL
Create AST node in __add__
Append created node to AST
  What if I have another 5-10 AST nodes?
  Do I need to copy-paste the append code 5-10x?
  Where to append?
def __add__(self, b):
node = AddNode(self, b)
ast.func.block.append(node)

## Slide 11: decorator/
A function that returns a function that hooks a functions
  wrapper.py
The decorator module: package.py
An abusive usage (?)
  init.py
pip --user install decorator

## Slide 12: Recap: Trace-based DSL
Create AST node in __add__
Append created node to AST
  What if I have another 5-10 AST nodes?
  Decorator hooks each function
@ir_builder
def __add__(self, b):
return AddNode(self, b)

## Slide 13: Understanding Each Stage (CONT’D)
Decorator changes the “current” module to append

## Slide 14: Roadmap
Recap: A simplest 2-stage pipeline
Do we really understand every line?
  Decorator
  Partial
    Hardwar-ized Software Pipelining
    Bind the dataflow

## Slide 15: Recap: Understanding Each Stage
The logic of each stage: Adder

## Slide 16: Understanding Each Stage (CONT’D)
The logic of each stage: Driver

## Slide 17: Partially Bind Arguments
partial.py
Fixes function arguments one by one

## Slide 18: Understanding Each Stage (CONT’D)
We only have void-call in Assassyn
adder0 = bind adder.a = cnt[0]
adder1 = bind adder0.b = cnt[0]
call adder1

## Slide 19: Understanding Each Stage (CONT’D)
I only have void-call in my IR
adder.a.push(cnt[0]) // %1
adder.b.push(cnt[0]) // %2
call adder [%1, %2]

## Slide 20: Question
How can we have a FIFO?
Why do you design void-call with binds?

## Slide 21: Recap: Micro-architectural Support
Each function is a pipeline stage
Implicitly,
  All the stage registers are FIFOs
  A Counter SM is imposed to bookkeep executions
Counter State Machine
  Each function call increases
  Each execution decreases
  Counter != 0 enables stage execution

## Slide 22: Verilog: How to manage a FIFO?
Why is Verilog so hard to write?
3×3=9
  3 Valid/Ready/Payload
  In/Out/Wire
Pusher
Pushee
push_data
push_valid
FIFO_ready
User
pop_data
pop_valid
pop_ready

## Slide 23: Verilog: Fake it until you make it.
Pusher
Pushee
push_data
push_valid
FIFO_ready
User
pop_data
pop_valid
pop_ready
logic [WIDTH - 1:0] q[$];
always @(posedge clk or negedge rst_n) begin
if (!rst_n) begin
pop_valid <= 1'b0;
pop_data <= 'x;
end else begin
if (pop_ready) q.pop_front();
if (push_valid) q.push_back(push_data);
if (q.size() == 0) begin
pop_valid <= 1'b0;
pop_data <= 'x;
end else begin
pop_valid <= 1'b1;
pop_data <= q[0];
end end end
Initialization
pop_ready
  q.pop()
push_valid
  q.push(data)

## Slide 24: FIFO: A Penetrable Design
back++

## Slide 25: Summary: Why do we call it RTL?
Software engineering is imperative
  a.push(x)
  a.pop(x)
Architecture description is graph connection
  Connection transfers register data from upstream to downstream based on state machine controls
  push_valid/pop_valid
  Transfers data from FIFO buffer to pop_data reg

## Slide 26: Question
How can we have a FIFO?
Why do you design void-call with binds?

## Slide 27: Systolic Array: A Simplest Dataflow Arch.
4 3 2 1
4 3 2 1
4 3 2 1
4 3 2 1
4 3 2 1
4 3 2 1
4 3 2 1
4 3 2 1

## Slide 28: Systolic Processing Element (PE)
×
+
A
B
Reg
×
+
A
B
Reg
×
+
A
B
Reg
A microarchitectural zoom-in

## Slide 29: Summary
N3 v.s. 2N2
Exec. Time = (Amount of work) / (Comp. Power)
What is the source of acceleration?
  Instruction Parallelism

## Slide 30: Be careful about the timing!
×
+
A
B
Reg
1
1
2
3
4
A friendly case
×
+
A
B
Reg
1
1
2
3
4
How many C should be buffered?
Assuming we have back pressure
C
+

## Slide 31: What if I do not have enough buffer?
×
+
A
B
Reg
1
1
2
3
4
A friendly case
×
+
A
B
Reg
1
1
2
3
4
C
+
Buffer filled. Then back pressured. C stops.

## Slide 32: What if I do not have enough buffer?
×
+
A
B
Reg
1
1
2
3
4
A friendly case
×
+
A
B
Reg
1
1
2
3
4
C
+

## Slide 33: Wait… Is there something missing?
Bind the dataflow
There are too many “bind”s in Python, which one?
3
1
2
PE1 cannot call PE2 alone because it has one argument input from PE3
from functools import partial
def foo(a, b):
return a + b
goo = partial(foo, 5)
# equivalent to foo(5, 10)
goo(10)
Software Programming
  foo(*args): args are all in caller
Hardware Design/Impl.
  Data from A & B flow to C

## Slide 34: Bind the dataflow (CONT’D)
3
1
2
PE1 can call PE2’s bound handle with argument from PE3 fed
# init pe[i][j] w/ PE()
# top function
for i in 1..5:
for j in 1..5:
pe[i][j].build(pe[i+1][j],
pe[i][j+1].bound)
# module
class PE:
def __init__(self):
self.north = Port(8)
self.west = Port(8)
def build(south, east):
bind south(north=self.north)
async east(west=self.west)
Higher-order Function
  A function that returns a function
  Constructing pipeline stage is constructing a parameterized function

## Slide 35: Homework: Weight-Stationary Systolic Array
This systolic array is called psum stationary, which buffers the accumulator in each PE
Based on examples/systolic_array.py
Implement a weight stationary systolic array, which buffers weight in each PE

## Slide 36: Roadmap
Recap: A simplest 2-stage pipeline
Do we really understand every line?
  Decorator
  Partial
  Return

## Slide 37: Recap: What is this sign for?
Do you have a driver’s lic?
Did you use yield in Python?
Returned, but not fully returned.

## Slide 38: Recap: Understanding Each Stage
The logic of each stage: Adder
valid = self.a.valid() & \
self.b.valid()
wait_until(valid)

## Slide 39: Recap: Micro-architectural Support
Each function is a pipeline stage
Implicitly,
  All the stage registers are FIFOs
  A Counter SM is imposed to bookkeep executions
Counter State Machine
  Each function call increases
  Each execution decreases
  Counter != 0 enables stage execution
√

## Slide 40: Counter: A “FIFO” w/o Payload

## Slide 41: Recap: Micro-architectural Support
Each function is a pipeline stage
Implicitly,
  All the stage registers are FIFOs
  A Counter SM is imposed to bookkeep executions
Counter State Machine
  Each function call increases
  Each execution decreases
  Counter != 0 enables stage execution
√
√

## Slide 42: One last thing. What are these for?
These are unexplained yet.
What are those?
Cross stage combinational logics
IF
ID
EX
MA
WB
In Use
Decoder checks availability
  Set the in use to true
Write back releases availability

## Slide 43: Combinational pins across modules
IF
ID
EX
MA
WB
In Use
if !in_use[rs1:rs1] && !in_use[rs2:rs2]
# ...
return rs1, rs2
return rd
in_use <= in_use ^
(1 << id.rd) ^
(1 << wb.rd);
Key demand: Expose data across modules within a same cycle.

## Slide 44: Recap: Trace-based DSL
Expose the handle to values using return
Use these values in an aggregated module
if !in_use[rs1:rs1] && !in_use[rs2:rs2]
return rs1, rs2
return rd
Something like a global value, but defined locally
in_use = in_use ^
(1 << id.rd) ^
(1 << wb.rd);

## Slide 45: FIFO: A Penetrable Design
back++

## Slide 46: Summary: Why do we call it RTL?
Recap the FIFO case
  a.push(x)
  a.pop(x)
Transfers data from last stage register to the next
  Through combinational logics
  All the registers are exclusive
  Thus, no order is enforced among pipeline stages
  Theoretically, no order is enforced among stages

## Slide 47: Downstream Module
What is downstream?
  Module is upstream.
Why do we have downstream?
  Downstream has a topology because of combinational logics
Let’s look at the simulator

## Slide 48: Care! Downstream modules hurt timing!
What should you do to bypass a branch result?
  Combinational?
  Sequential?
IF
ID
EX
MA
WB