## Slide 1: Computer Architecture W5D1: Out of Order (OoO)
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Characterization
Assumption: All the architectures discussed are pipelined.
Instead of saying Tomasulo or other algorithms, I will characterize:
  In-/out-of-order
  (Non-)Speculative
  Single/Multi-issue

## Slide 3: Roadmap
Why OoO?
How OoO?

## Slide 4: Why out-of-order?
IPC>1?
  Superscalar
Why is out-of-order beneficial?
  RAW hazard
  RAW still a problem?
    Larger issue window!
What is essentially a RAW?

## Slide 5: Why out-of-order? (CONT’D)
Consider the code snippet below:
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
1
2
3
4
5
6
7
1
2
5
6
3
7
4

## Slide 6: Why out-of-order? (CONT’D)
A thread is a topological order of the instructions
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
1
2
3
4
5
6
7
1
2
5
6
3
7
4
4 is far away in latency cuz floating point operations take long, but operands valid early

## Slide 7: How out-of-order?
Opportunity: Essentially we only need a partial order to resolve RAW hazard.
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
1
2
3
4
5
6
7
1
2
5
6
3
7
4
Challenge: The definition of vN execution.

## Slide 8: How out-of-order? (CONT’D)
Challenge: The definition of vN execution
All the instructions should be
  In order
  Atomic
Contradiction w/ out of order!
  Arithmetics should be in order
  Roll back predictive instructions
  Each load/store should be in order

## Slide 9: Challenges (CONT’D)
Challenge: The definition of vN execution
Contradiction w/ out of order!
  Arithmetics should be in order
  Roll back speculative instructions
  Each load/store should be in order
Locate the precise state of execution
  Debugging
  OS management
  👉🏻 Same requirement as speculation

## Slide 10: Key Design: Reorder Buffer
ROB: Reorder Buffer
Magic Pipeline
Reorder Buffer

## Slide 11: Demystify the “Magic”
Dude, there is no magic in this world
Reorder Buffer
ID
IF
EX
Alloc
RF
C
R

## Slide 12: Writeback - Complete
Writeback is broken down to two parts
  Complete (C): Write inst results to ROB
  Propagate the results to instructions awaits
Reorder Buffer
ID
IF
EX
Alloc
RF
C
R

## Slide 13: Writeback - Retire
Writeback is broken down to two parts
  Retire (R): Commit the first batch of instructions completed to the register file
Reorder Buffer
ID
IF
EX
Alloc
RF
C
R

## Slide 14: Even harder! What about Load/Stores?
Atomic instructions are enforced by ROB
How are the orders of memory operations enforced?
  Imprecise memory is a even worse disaster than regs
Solution: Load/Store Queue (LSQ)
  LSQ holds speculative memory operations
  Store writes to LSQ when C-stage
  Store writes to memory when R-stage
  When loads execute, access both memory and LSQ

## Slide 15: LSQ: Load/Store Queue
Solution: Load/Store Queue (LSQ)
  LSQ holds speculative memory operations
  Store writes to LSQ when C-stage
  Store writes to memory when R-stage
  When loads execute, access both memory and LSQ
    Fast forward older store with the matching address from LSQ
  More modern design: separate L/S queue
More on this later

## Slide 16: Demystify the “Magic”
Reorder Buffer
ID
IF
EX
Alloc
RF
C
R
LSQ
D$
+
MA

## Slide 17: Demystify the “Magic”
Reorder Buffer
ID
IF
EX
Alloc
RF
C
R
LSQ
D$
+
MA

## Slide 18: How is reorder buffer allocated?
It seems to be trivial, a cyclic FIFO
Why does it matter?
Reorder Buffer
Front
Tail
rd
result
ROB will commit results to register file.

## Slide 19: Question: What if ROB is full?
It is a structural hazard
  The resource required is not available
  Stall for availability
What is the size of an ROB for not stalling?
(Pipeline Depth)×(Issue Width)
  Did you still member the cost of register writing?
  (Pipeline Depth)×(Issue Width)2

## Slide 20: Recap: We already had something like ROB before…
rename_entry = alloc_entry()
rename[rd] = rename_entry
r1_data = data[rename[rs1]]
++use[rename[rs1]]
r2_data = data[rename[rs2]]
++use[rename[rs2]]
IF
ID
EX
MA
WB
data[rename_entry] = result
if use[rename_entry] == 0 {
dealloc(rename_entry) }
Allocate a mapping entry each time
  This is a full delegate to the register
  Further read and write will be redirected to this mapped register

## Slide 21: What we discuss next is P6 architecture
If you still remember this…
Trends to have more stages for better frequency
  486 (1989): 5
  Pentium (1993): 7
  Pentium II (1997) / III (1999): 12
  Pentium 4 (2000-2007): 22
  Nehalem (2008): 20-24
  Haswell (2013) / Skylake (2017) / Cooper lake (2020): 14-19
A Tomasulo + ROB
  Though I do not know what is Tomasulo…
Should be something here…

## Slide 22: Can we use ROB for the similar purpose?
Reorder Buffer
Front
Tail
rd
result
ROB will commit results to register file.
Yes! But we need a Tag Mapper
  Up-to-date value is valid in ROB
  Up-to-date value is invalid in ROB (but will be valid soon)
  Up-to-date value in Reg File
…
TMap

## Slide 23: Instruction Dispatching: Reservation Station
Slightly more complicated than decoding
TMap
rd
rs1
rs2
t1
t2
rd
rs1
rs2
t1
t2
rd
rs1
rs2
t1
t2
rd
rs1
rs2
t1
t2
Read register status
Update register status in RS
Int
FP
LD
ST
Reservation
Station
Reservation station tracks the data validity
Once both valid, data will be read from the correct source
  ROB
  RF

## Slide 24: Instruction Dispatching: Read Operands
Slightly more complicated than decoding
…
TMap
Reorder Buffer
RF
rs1
Copy the valid value to operand buffer
t1
t2
&
Validity

## Slide 25: Issue to Execution
rob
v1
v2
op
valid
…
…
…
FU
Reorder Buffer
Once the data are both available, they are copied to the operand buffer of an FU
FUs’ buffer is a FIFO
FU writes to ROB entry the result

## Slide 26: Put it all together.
A bookkeeping-logic decoupled implementation
Care! Too many indirect addressing
ID
IF
C
R
RS
Allocate on ROB
ROB
TMap
Check/update data validity
Writes result
Reg
Commit result
EX
Bookkeeping
Logics

## Slide 27: Back to this example
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2

## Slide 28: Look into this example
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f0
f1
f2
r1
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
R0
R0
ID

## Slide 29: Look into this example – Cycle 1
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f0
f1
f2
r1
ROB0
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB0
R0
r1
R1
Allocates execution entry
ID

## Slide 30: Look into this example – Cycle 2
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
f0
f1
f2
r1
ROB0
ROB1
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB0
ROB1
R0
r1
f0
R1
ROB0
Not only allocates execution entry, but also redirects f1 to ROB renaming
Load issued for execution
EX
ID

## Slide 31: Look into this example – Cycle 3
MA
RS
ID
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
√
f0
f1
f2
r1
ROB0
ROB1
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB0
ROB2
ROB1
R0
r1
r1
f0
R1
ROB1
ROB0
Not yet valid, wait!
Not yet valid, wait!

## Slide 32: Look into this example – Cycle 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
r1
√
f0
f1
f2
r1
ROB0+
ROB1
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB3
ROB2
ROB1
R0
r1
r1
f0
R1
4
ROB1
ROB0
C
RS
RS
ID
Finished!
Set the tag “valid in ROB”
Broadcast to users
Allocates new entry for int add!

## Slide 33: Look into this example – Cycle 5
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
r1
√
f0
f1
f2
r1
ROB4
ROB1
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB3
ROB4
ROB2
ROB1
R0
r1
r1
r1
f0
R1
4
ROB1
ROB0
R
EX
RS
EX
ID
Committing to RF!

## Slide 34: Look into this example – Cycle 6
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
r1
√
√
√
f0
f1
f2
r1
ROB1+
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB4
ROB2
ROB1
R0
r1
r1
f0
R1
ROB1
ROB0
R
C
RS
C
RS
Updated to the latest value!
Addition is done, and broadcast r1 to RS
Update f2 to “valid in ROB”

## Slide 35: Look into this example – Cycle 7
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
r1
√
√
√
f0
f1
f2
r1
ROB1+
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB4
ROB2
ROB1
R0
r1
r1
f0
R1
ROB1
ROB0
R
R
EX
R?
EX
Update f1 to the latest value!
Cannot retire. Still instructions before!
Committing to RF…

## Slide 36: Look into this example – Cycle 8
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
√
√
√
f0
f1
f2
r1
ROB4
ROB5
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB4
ROB2
ROB5
R0
r1
r1
f0
R1
ROB1
ROB4
R
R
MA
R?
MA
ID
Update the new compute!
Use the latest value in RS!

## Slide 37: Look into this example – Cycle 9
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
√
√
√
f0
f1
f2
r1
ROB4+
ROB5
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB2
ROB5
R0
r1
f0
R1
ROB1
ROB4
R
R
C
R?
C
ID
Update the new compute!
Use the latest value in RS!
Valid in ROB

## Slide 38: Look into this example – Cycle 10
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
r1 = r1 + 4
f1 = *X(r1)
f2 = f0 * f1
*Z(r1) = f2
Inst
0
1
2
3
4
5
6
RD
V
f1
f2
×
√
√
√
f0
f1
f2
r1
ROB4+
ROB5
ROB3
INT
LD
ST
FP1
FP2
FU
0
1
2
3
4
RD
ROB2
ROB5
R0
r1
f0
R1
ROB1
ROB4
R
R
R
R?
R
EX
ID
Update the new compute!
Retire together, head += 2!
Committing to RF!

## Slide 39: Summary: P6
It was popular for a while
Relatively easy to implement
At what cost then?
  Too many data movements

## Slide 40: Too many data movements
ROB to Reg
TMap to RS
ROB/Reg to Operand Buffer
ID
IF
C
R
RS
Allocate on ROB
ROB
TMap
Check/update data validity
Writes result
Reg
Commit result
EX
Bookkeeping
Logics

## Slide 41: Alternative: MIPS R10K
Big Idea: Use a big physical register file to hold all data without copies
   Registers are only for FUs
   ROB is just a side data structure for reordering

## Slide 42: Alternative: MIPS R10K (CONT’D)
Architecture logic registers are fully gone, just like other register renamings
Fundamental Change: TMap
  Instead of having a cyclic FIFO for ROB-based register renaming, a free list is maintained to allocate registers
  ROB commitment frees allocated register

## Slide 43: Key Challenge: Maintaining Renaming
Consider the example right
We have logic register r1-3
Physical register p1-7
  Initially, p1-3 maps to r1-3
Key question
  When to free the allocated physical register?
  Wrong Answer: Free it upon retirement.
  No register copy to it!
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3

## Slide 44: Allocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
p4 = p2 + p3
r1
p1
p4
r2
p2
p2
r3
p3
p3
p1,p2,p3,p4,p5,p6,p7

## Slide 45: Allocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
p4 = p2 + p3
p5 = p2 + p4
p1,p2,p3,p4,p5,p6,p7
r1
p1
p4
p4
r2
p2
p2
p2
r3
p3
p3
p5

## Slide 46: Allocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
p4 = p2 + p3
p5 = p2 + p4
p6 = p2 + p5
p1,p2,p3,p4,p5,p6,p7
r1
p1
p4
p4
p6
r2
p2
p2
p2
p2
r3
p3
p3
p5
p5

## Slide 47: Allocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
p4 = p2 + p3
p5 = p2 + p4
p6 = p2 + p5
p7 = p6 / p5
p1,p2,p3,p4,p5,p6,p7
r1
p1
p4
p4
p6
p6
r2
p2
p2
p2
p2
p7
r3
p3
p3
p5
p5
p5

## Slide 48: Deallocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
When 1st instruction is done, which one to dealloc?
p4 = p2 + p3
p5 = p2 + p4
p6 = p2 + p5
p7 = p6 / p5
p1,p2,p3,p4,p5,p6,p7
r1
p1
p4
p4
p6
p6
r2
p2
p2
p2
p2
p7
r3
p3
p3
p5
p5
p5
Not p4, it is still in use by next instruction

## Slide 49: Deallocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
When 1st instruction is done, which one to dealloc?
p4 = p2 + p3
p5 = p2 + p4
p6 = p2 + p5
p7 = p6 / p5
p1,p2,p3,p4,p5,p6,p7
r1
p1
p4
p4
p6
p6
r2
p2
p2
p2
p2
p7
r3
p3
p3
p5
p5
p5
Why do we bother to keep p1?

## Slide 50: Deallocate Renaming
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
When 2nd instruction is done, which one to dealloc?
p4 = p2 + p3
p5 = p2 + p4
p6 = p2 + p5
p7 = p6 / p5
p1,p2,p3,p4,p5,p6,p7
r1
p1
p4
p4
p6
p6
r2
p2
p2
p2
p2
p7
r3
p3
p3
p5
p5
p5
Why do we bother to keep p3?

## Slide 51: Deallocate Renaming: Conclusion
r1 = r2 + r3
r3 = r2 + r1
r1 = r2 * r3
r2 = r1 / r3
Consider the example below
Free the register allocated to this logic register last time
Why?
All insts themselves will not read their retired value
p4 = p2 + p3
p5 = p2 + p4
p6 = p2 + p5
p7 = p6 / p5
r1
p1
p4
p4
p6
p6
r2
p2
p2
p2
p2
p7
r3
p3
p3
p5
p5
p5

## Slide 52: Implementation
Reorder Buffer
  No data now
  RD → Physical Tag and Old Physical Tag
  Old Tag for free-ing (not for free) entries
Rolling back Map Table and Free List
  Option I: Rolling back one by one
  Option II: Rolling back upon check points

## Slide 53: LSQ: Load/Store Queue
Solution: Load/Store Queue (LSQ)
  LSQ holds speculative memory operations
  Store writes to LSQ when C-stage
  Store writes to memory when R-stage
  When loads execute, access both memory and LSQ
    Fast forward older store with the matching address from LSQ
  More modern design: separate L/S queue
More on this later

## Slide 54: LSQ: Load/Store Queue
Atomic instructions are easy to OoO
  Because they are side-effect state-free
  Same register inputs, same output
  Tags manages execution scheduling
What make loads special?
  Register & memory inputs
  Memory modified by store
  Register tags does not tell you all dependences

## Slide 55: LSQ? Separated LQ & SQ!
Writes stores to memory in order
  Done by SQ
Store-load forwarding
  Loads read values from older un-retired stores
  Also done by SQ
Memory order violation detection/avoidance
  Speculative loads (more on this later)

## Slide 56: Store Queue: A Zoom-in
Store is like other FU
  2 register inputs: value, and address
  A non-register input
Store Queue (SQ)
  In-flight store address/value
  Just like ROB a cyclic FIFO
  Addresses are associatively search-able
  Size: Heuristically: 15-20% of ROB
Address
Value
A Store Queue Entry

## Slide 57: Store Queue: A Zoom-in
Store
  Dispatched by RS: Allocate SQ entry
  Execute: Write address and data into Q
  Retire: Write to memory, free head
How does it interact with load?
  Dispatched by RS: Record the current tail as load position
  Execute: More on this next…
Address
Value
A Store Queue Entry

## Slide 58: OoO of Load
Parallel w/ sending memory request
Sends address to SQ
  Compare all addresses in SQ
  Select all matching addresses
  Find the youngest store older than this load
  Older than this load: Takes effects
  Youngest: Takes newest effects
Load Addr
Age
Addr
Addr
Addr
Addr
Addr

## Slide 59: Load Scheduling
P6 is OoO, but how does memory load?
Loads are OoO with respect to (wrt) other loads
Stores are OoO wrt other loads
Loads in-order wrt older stores
   Simple & correct!
   Limits performance

## Slide 60: Speculative Memory Scheduling
Observation: 10% of loads are from SQ
It is possible an store’s address is unknown while loads’ address won’t match
Issue memory early to increase performance
But what if it does match?
  Detect and fix.

## Slide 61: Load Queue: A Zoom-in
Load
  Dispatched by RS: Allocate LQ entry
  Exec: Write addr into LQ entry
How does it interact with store?
  Dispatch: Record the current LQ tail as store position
  Exec: More on this next…

## Slide 62: Detecting Memory Violations
Sends address to LQ
  Compare all addresses in LQ
  Select all matching addresses
  Find load younger than this store
    A load executed before store
    Violation
    Flush the load and restart!
Store Addr
Age
Addr
Addr
Addr
Addr
Addr

## Slide 63: More Opportunities…
Store/Load violations are often consistent because of the program semantics
Remember! .text section has no write permission, so the program does not change
Opportunity: Hybridize conservative and speculative
  Predict violations on load/store pairs
  Use conservative on violated ones and use aggressive for others

## Slide 64: ILP: Instruction-Level Parallelism
OoO is a zigzag solution
  Threads in full order
  OoO exploits the partial order
  ROB recovers the full order