## Slide 1: Computer Architecture
Jian Weng
Computer Science
CEMSE, KAUST
W1D1: An Intro to Computer System

## Slide 2: Roadmap
Misc
  Self introduction
  Course policies
Why do we learn system?
How do we learn system?
Why bits?

## Slide 3: Misc
Who am I?
  B.Eng. SJTU ACM Honored Class (2013-2017)
  Ph.D. UCLA Computer Science (2017-2023)
  Assistant Prof at King Abdullah University of Science and Technology (KAUST) (2024-)
Why do I teach this?
  To flatten your learning curve of compilers, architecture, and operating systems

## Slide 4: Policies
No Electronic Devices
Attendance
  Absence will invalidate all your related grades
  Ask your roommates to show up
Generative AI
  Can you validate its answer somewhere else?
    Google it! Use your own understandings!
    Try it! Get your hands dirty!
Plagiarism
  No unauthorized collaboration
  List all the sources and resources you used

## Slide 5: Policies (CONT’D)
Grading
  30%
    Quizzes right after instructions
    Homework labs: No worries, very simple and useful
  70%
    Final project: 5-stage pipelined CPU
Teaching
  Feel free to interrupt me when confused
  But I will decide what to teach you

## Slide 6: Syllabus
An Intro to Computer Systems (W1-W6, Summer)
  Flatten your learning curve for compilers and archs
An Intro to Computer Architecture (W1-W10, Fall)
  Let’s do this here!
Implementing a simple 5-stage pipeline CPU
  In Register-Transfer-Level (RTL) Language

## Slide 7: Resources
I learned most of these knowledge from
  Computer System: A Programmer’s Perspective
  Computer Organization and Design
  Computer Architecture: A Quantitative Approach

## Slide 8: Roadmap
Misc
Why do we learn system?
  System is everywhere
  System is beyond system
How do we learn system?
Why bits?

## Slide 9: Why do I need to learn systems?
Marxism: Substructure (base) and superstructure
  Base determines the superstructure
What does a typical LLM do?
  Predict the probability of the next token
What is a basic building block of an LLM?
  Transformer
What does a transformer do?
  Mix data using matrix multiplications

## Slide 10: How LLM works: A Typical Transformer Block
Softmax
Dense
Linear
Dense
Linear
Dense
Linear
Embeddings
Legend
Attention
Projection
Act.
???

## Slide 11: Which program is faster?
Why? This is the effort of compiler and arch together!

## Slide 12: What does all these tech sepc mean?
What is clock freq?
What is cache?
What is core and thread?
Why does TDP matter?
Source: https://www.amd.com/en/products/processors/desktops/ryzen/9000-series/amd-ryzen-9-9950x3d.html

## Slide 13: Computers only recognizes binaries (0/1)
What does binaries mean?
Why do we have to stick to binaries?
Source: The Matrix (1999)

## Slide 14: What are we goanna learn?
How is a program running on CPU?
Why do we need a compiler?
What does software cracking do?
What does GHz and L1/L2/L3 cache mean when buying a computer?
How can I compile code for/from others to use?
What is the implication of Moore’s Law?
What does a LLM typically do?
Why computer system matters for other areas?

## Slide 15: Summary: Did I convince you computer system is both useful and interesting?
What is computer system then?

## Slide 16: Why can we write once, run everywhere?
C
Python
JavaScript
Some Magic
What is the magic?
Compiler
Interpreter
OS

## Slide 17: What is a computer system?
Define the inputs and outputs
Solve the problem from one end (inputs) to the other end (outputs)
System essentially encapsulates all the low-level details while retaining acceptable performances
Any problem in computer science can be solved by another layer of indirection (abstraction).
——Butler Lampson. Principles for Computer System Design. Turing Award Lecture. February 17, 1993

## Slide 18: Exemplifying Systems
Compiler
  Input: High-level Language
  Output: Compiled Binaries
  System
    Translate high-level language
    Optimize the performance
    Generate the compiled binaries
Operating System
  Input: User Interactions
  Output: Program Executions
  System
    Manage the user interactions with devices
    Schedule the program executions

## Slide 19: What are your inputs to modern computers and outputs to you?
Inputs
  Mouse clicks
  Keyboard types
  Gaming controllers
  Cameras
Outputs
  Screen
  Audio
Application oriented!

## Slide 21: System is a system engineering
Today, system stack is a “normal”
  Clear boundary b/t sw/hw
  Recompile to run
  Or even write once run everywhere
But it wasn’t decades ago
Beyond system engineering itself, system is a philosophy.
Application
Programming Language
Compiler
Executable
Operating System
Architecture
EDA
Silicon
Driver
Devices
Bare Metal
SDK
Hardware
Software

## Slide 22: System is an engineering philosophy
What is a frontend and backend in website/application design?
  FE: User interface, run on users’ devices
  BE: Server processing, run on machines in data centers
  B/t: POST protocol
Application
Programming Language
Compiler
Executable
Operating System
Architecture
EDA
Silicon
Driver
Devices
Bare Metal
SDK

## Slide 23: Engineering Philosophy: Manage Legacies
A rule of thumb is to develop it incrementally
Then inevitably you need to manage the legacies
The legacy wrapper creates illusion that old function is
still there

## Slide 24: Roadmap
Misc
Why do we learn system?
How do we learn system?
Why bits?
  A quick tool to digital signal processing

## Slide 25: How do we learn computer systems?
Computer science is NOT unique.
  Re-practice the philosophy from existing industry divisions.
  Labor division, and modular design
Computer science is unique
  You are both a user and a developer
  Everything can be tried immediately

## Slide 26: Bit: Basic Information Building Block; But why?
What is bit?
  Not this bit
A good enough analogy for non-EE person (just like me)
  A valve and fluid model

## Slide 27: Valve and Flow – Building block of building block
We use some fluid to push the valve
  High pressure represents 1
  Low pressure represents 0
Valve opens or closes the way for the fluids
  There is a small hole on the mover in the middle which allows fluid to flow through
High
(On)
High
(Off)
N-Valve
P-Valve
Low
(On)
Low
(Off)
hole

## Slide 28: Inverter - One of basic building blocks
What does it invert?
High
Low
Out
N-Valve
P-Valve
In
Low
(0)
High
Low
High
(1)
N-Valve
P-Valve

## Slide 29: Inverter - One of basic building blocks
What does it invert?
High
Low
Out
N-Valve
P-Valve
In
High
Low
Low
(0)
N-Valve
P-Valve
High
(1)

## Slide 30: NAND – Another basic building block
NAND: NOT (A & B)
NAND itself is Turing Complete
  A & B
  A | B
  A ^ B
out
A
B
High
Low
High

## Slide 31: Quiz: Use NAND to write all the remaining operators
~A =
A & B =
A | B =
A ^ B =
A A
~(A A)
(~A) (~B)
(A & ~B) (~A & B)
Hint: System is all about encapsulation. If you have one operator implemented, just use it for further writeups.

## Slide 32: Truth table? Look-up table!
A truth table of NAND
  What if we regard it as a 4-sized array
  [1, 1, 1, 0][idx]
  k-bit input we need a (2^k)-sized array
A | B | Result
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 33: What if the table is too big?
Say, we need a 32-bit addition, a + b
Nobody does 2^64 look up table for the results
What do we do?
1 2 8
1 2 8
+
2 5 6
1
^
&
^
^
&
|
&
A0
B0
O0
A1
B1
O1
&
|
Carry
Carry

## Slide 34: Why do we need this?
This is the so-called “synthesis”, which converts arithmetics to silicon gates
This is the matter base of binaries
1 2 8
1 2 8
+
2 5 6
1
^
&
^
^
&
|
&
A0
B0
O0
A1
B1
O1
&
|
Carry
Carry

## Slide 35: Why do we need this? (CORRECTED)
This is the so-called “synthesis”, which converts arithmetics to silicon gates
If you do a+b in Verilog, the synthesizer will take all the for you
1 2 8
1 2 8
+
2 5 6
1
^
&
^
^
&
|
&
A0
B0
O0
A1
B1
O1
&
|
Carry
Carry
c[i], o[i] =
full_adder(a[i], b[i], c[i-1])

## Slide 36: Egg
Bureau of Industry and Security
  Code of Federal Regulation Part 774

## Slide 37: Summary: Bits are the basic building blocks of information.
Application
Programming Language
Compiler
Executable
Operating System
Architecture
EDA
Silicon
Driver
Devices
Bare Metal
SDK

## Slide 38: Summary: Bits are the basic building blocks of information.
Compiler
Executable
Operating System
Architecture
EDA
Silicon
Bare Metal
This was what we discuss just now

## Slide 39: Summary: Bits are the basic building blocks of information.
Instruction Set Architecture (ISA)
  Instruction Set: A specification to the instructions
  Each instruction can be encoded in bits for machine inputs
    Program is also data
    Each instruction cannot do something too complicated (?)
Compiler
Executable
Operating System
Architecture
Bare Metal

## Slide 40: Program is also data
Thread: A thread of continuous instructions to execute.

## Slide 41: Instruction Encoding
X86
  jmp label
  EB FE
RISCV