## Slide 1: Computer Architecture W3D1: A Real Intro Computer Architecture
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Roadmap
What is an architecture?
What are the laws?
  How to measure the performance?
  How to improve the performance?
  Why should we have better performance?

## Slide 3: What is architecture?
ISA: Instruction Set Architecture
  Something executes a set of instructions
  The organization of the components to execute
A design of the underlying “something”

## Slide 4: Globalization & End2end
Chip design
Chip tape-out

## Slide 5: What is a Quantitative Approach?
(Nearly) Everyone learned (or will learn) computer architecture from this book
But what is the specific quantitative approach?
  Macro: Where to have the performance?
  Micro: How do we achieve this?

## Slide 6: Quantitative Approach 1 – The Program Exec. Time
Execution Time = #Instructions × (Time per Instruction)
Execution Time = Amount-of-work / Computing Power
Where does time go?
But, it sounds like a correct non-sense!
What insight does it reveal?
  RISC v.s. CISC
t=s/v
s=tv

## Slide 7: Quantitative Approach 1 – The Program Exec. Time
#instructions
  Faithfully execute the program, just like PoW
  Reduce the number of instructions?
Time per Instruction
  How to decrease the amortized time per instruction?
Execution Time = #Instructions × (Time per Instruction)
Distance = Time × Velocity

## Slide 8: The Debate of RISC and CISC
RISC: RISCV, ARM, MIPS
  Many general registers: RISCV has nearly 20
  3-address opcode: $rd, $rs1, $rs2
  Instruction operands in registers
  Simple operations
CISC: X86
  Few general registers: X86 just has 8
  2-address opcode: something like $rd += $rs
  Instruction operands IMR (imm, mem, reg)
  Complex operations (?)
# RISCV-like
ld $t3, a($t1)
ld $t4, b($t1)
add $t5, $t4, $t3
sw $t5, a($t1)
# x86-like
add a(%eax), b(%eax)

## Slide 9: Microcode: A bridge from CISC to RISC
Frontend: CISC instructions
  One day, Intel finds its CISC ISA is too complicated to be decoded by dedicated circuits
Backend: Each complicated instruction would be broken down to simple RISC-like ones
This is also widely used in performance modeling [1]
[1]: The gem5 simulator, https://www.gem5.org/
# RISCV-like
ld $t3, a($t1)
ld $t4, b($t2)
add $t5, $t2, $t3
sw $t5, a($t1)
# x86-like
add a(%eax), b(%eax)

## Slide 14: Quantitative Approach 2 – Amdahl’s Law
The speedup of a system you can earn from optimizing a portion of this system is dominated by the original % of this portion
👉🏻 Optimize the most critical portion first!

## Slide 15: Amdahl’s Law (CONT’D)
Say, in a system, memory access occupies 60%, while computation occupies 10%.
  What if we make the computation 1 million × faster?
    Execution Time:
  What if we halve the memory access time, what do we get?
The original execution time w/ optimized part excluded
Optimized execution time
Execution Time:
Speedup:

## Slide 16: Amdahl’s Law in the Multi-core Era [1]
Quiz: What if of a program is parallelizable and we have cores?
  Execution Time:
Goal: Under a fixed budget, how can we best balance the relation b/t core# and single-core power? [1]
[1] M. D. Hill and M. R. Marty, "Amdahl's Law in the Multicore Era," in Computer, vol. 41, no. 7, pp. 33-38, July 2008, doi: 10.1109/MC.2008.209.
Sequential Part
Parallelized

## Slide 17: Amdahl’s Law in the Multicore Era (CONT’D)
Say, we assume:
  units of budget
  of the application is parallelizable
  If I spend units of budget on each core, I get computing power, and n/r cores
    Execution Time =
Why ? You are favoring multi-core too much!
Amount of work
Computing power

## Slide 18: A (Not that solid) justification of
Did you played overclocking before?
  Speedup the clock frequency to speedup your machine
  Or tune down the frequency for better energy savings (ETH PoW Mining)

## Slide 19: Recap: The Valve-Liquid Model
NAND: NOT (A & B)
NAND itself is Turing Complete
  A & B
  A | B
  A ^ B
out
A
B
High
Low
High

## Slide 20: A (Not that solid) justification of
Did you played overclocking before?
  Speedup the clock frequency to speedup your machine
  Or tune down the frequency for better energy savings (ETH PoW Mining)
The power of an integrated circuit
  , where
  Therefore, while perf

## Slide 21: Amdahl’s Law in the Multicore Era
Say, we assume:
  units of budget
  of the application is parallelizable
  If I spend units of budget on each core, I get computing power
Then the performance looks like
  Exec Time:
Sequential exec time
Parallelizable sequential exec time
Divided by number of cores
Speedup over a core w/ 1-unit of budget

## Slide 22: Amdahl’s Law in Heterogeneous Multicore Era (CONT’D)
Say, we have:
  units of budget
  of the application is parallelizable
  If I spend units of budget on each core, I get computing power
  A super core occupies units, and cores with 1 unit
  Big core for sequential, and all core for parallelization
Exec Time:
Sequential exec time
Big-core computing power
Small-core computing power
Speedup over a core w/ 1-unit of budget

## Slide 23: Put them together!
Heterogeneous curves are higher then homogeneous one!
It is good to hybridize big/small cores when fixing the power budget.
Wait? Is it useful?

## Slide 24: Amdahl’s Law in Heterogeneous Multicore Era (CONT’D)
This is widely adopted in:
  your cell phones (Apple since A7 in 2010s)
  and laptops (Intel AlfredLake in 2020s)
Relations among the Academia, and the Industries

## Slide 25: What if we make it even better?
Say, we have:
  units of budget
  of the application is parallelizable
  If I spend units of budget on each core, I get computing power
  This system can be used as a -core when sequential
  This system can be used as a N-core when parallelizable
Exec Time:
Sequential exec time
N small cores, each computing power is 1
Speedup over a core w/ 1-unit of budget

## Slide 26: Put them together! (CONT’D)
Magic?
No, more engineering and research effort 

## Slide 27: Summary
Heterogeneity brings more potential on the performance under a same budget
However, it also urges us to seek the better mechanisms on both software stack and hardware design to take advantage

## Slide 28: Challenges and Opportunities on Post-Moore’s Law Era
Chart: 
Single-Thread Perf. (SPEC-INT × 10³) | 83.5363 | 50.0286 | 55.7306 | 90.5798 | 177.8279 | 273.842 | 321.9678 | 239.2799 | 349.1152 | 598.8854 | 1027.3508 | 410.4698 | 922.2396 | 973.3774 | 667.1427 | 1382.3722 | 1810.5582 | 1274.8784 | 1762.3564 | 827.8826 | 1459.0242 | 3554.5224 | 2308.2415 | 1144.4419 | 2713.8994 | 1860.0784 | 3367.7803 | 4782.8581 | 5473.7033 | 6264.3354 | 4293.5102 | 6264.3354 | 9389.798
 | 20535.2503 | 36600 | 21100 | 37700 | 42000 | 25800 | 46000.7 | 39000.4 | 33000.6 | 31000.8 | 59000 | 33000.7 | 59000.6 | 59000.9 | 66000.4 | 65000.4 | 66000.1 | 73900.2 | 77900.2 | 83600.3 | 90900.2 | 78300.4 | 99000 | 97200 | 105300 | 10181.5172 | 11341.944 | 13335.2143 | 18938.4203 | 16548.171 | 21096.9051 | 17000.7762 | 21096.9051 | 18938.4203 | 21096.9051 | 35226.9465 | 23501.4008 | 31622.7766 | 14074.6466
Source: https://github.com/karlrupp/microprocessor-trend-data/
Why?
Why should we have better perf?
Why can’t we have expected perf?

## Slide 29: Why should we get more performance?
Credits to OpenAI DALL·E
CPU: A Data Factory
  Manufacturing: Program
  Raw Material: Data
  Product: Program Output
  Transistors: Budget for the workers and assembly lines
// Original C Code
for (i=0; i<n; ++i)
c[i] += a[i] * b[i];
( )
×n
( )
×n
( )
×n
Why should we have better perf?
Why can’t we have the expected perf?
What happens in CPU?
What happens to the program?

## Slide 30: Executing the assembly code? Organizing an assembly line!
Credits to OpenAI DALL·E
IF: “I read the manual for instructions!”
ID: “I check the data availability!”
EX: “I do the computation!”
MA: “I am the warehouse keeper!”
WB: “I check in the results!”
CPU: A Microprocessor
  Memory: Warehouse
  Registers: Handy place for compute-ready data

## Slide 31: Single-cycled Machine
A long critical path
Simple designs

## Slide 32: Recap: Critical Path
Or how good or bad is this solution?
^
&
^
^
&
|
&
A0
B0
O0
A1
B1
O1
&
|
Carry
Carry
^
^
&
|
&
A2
B2
O2
&
|
Carry
Repeat this block next 31 times
…
Pros: It works, and it is simple!
Cons: Slow... The longest path is linear to the bit width.

## Slide 33: Recap: The Valve-Liquid Model
NAND: NOT (A & B)
NAND itself is Turing Complete
  A & B
  A | B
  A ^ B
out
A
B
High
Low
High
Stage Registers: Some container for the inter-stage results

## Slide 34: Recap: The CPU Spec.
What is clock freq?
What is cache?
What is core and thread?
Why does TDP matter?
Source: https://www.amd.com/en/products/processors/desktops/ryzen/9000-series/amd-ryzen-9-9950x3d.html

## Slide 35: The Waveform (Comb & Seq)
Clock: Periodically generate pos and neg signal
Reg: Can only be written at pos-edge, but the result will take effect in next post-edge.

## Slide 36: The Waveform (Comb & Seq)
Clock: Periodically generate pos and neg signal
Reg: Can only be written at pos-edge, but the result will take effect in next post-edge.
Comb is immediately effective
Seq is asynchronized

## Slide 37: 5-stage Pipelined Machine
Stage registers among stages for shorter critical path
More complicated logics for interlocking

## Slide 40: Characterization
Assumption: All the architectures discussed are pipelined.
Instead of saying Tomasulo or other algorithms, I will characterize:
  In-/out-of-order
  (Non-)Speculative
  Single/Multi-issue

## Slide 41: Characterization
Assumption: All the architectures discussed are pipelined.
Instead of saying Tomasulo or other algorithms, I will characterize:
  In-/out-of-order
  (Non-)Speculative
  Single/Multi-issue

## Slide 42: What are the interlocks for?
Hazards: something the arch has to comply to have the semantics maintained
Types of hazards
  Resource hazard
  Data hazard
  Control hazard

## Slide 43: Data Hazard
Enforcing data dependences within a centralized register file
{Read, Write} x {Read, Write}
  Why not 4 hazards?
Assuming, we already know the trivial solution
  Wait until it works.

## Slide 44: Data Hazard – RAW
Read after write
  This is the only “real hazard”
ADD R1, --, --
SUB --, R1, --

## Slide 45: RAW – Bypassing
Before ADD data is committed to register file
MA
WB
Why?
  ADD has nothing to do with memory right?
ADD
EX
Decode
A
B
Sel
MA
B is symmetric to A, but to avoid over complicated Fig, it is omitted
WB

## Slide 46: Diverged: A Uniform Interfacing
Why cannot we bypass WB?
Both ADD and LOAD are writing to register!
ADD
EX
Decode
A
B
Sel
MA
B is symmetric to A, but to avoid over complicated Fig, it is omitted
WB
LOAD --, --, --
ADD --, --, --

## Slide 47: RAW – Fully Bypassing
Before ADD data is committed to register file
Remember to bypass from MA even it is an ADD!
Even from WB!
ADD
EX
Decode
A
B
Sel
MA
B is symmetric to A, but to avoid over complicated Fig, it is omitted
WB

## Slide 48: Data Hazard – WAR
Write after read
DIV --, R1, --
SUB R1, --, --

## Slide 49: WAR – A Zoom in
A maybe good enough demo
DIV --, R1, --
SUB R1, --, --
Read R1
Register File
…
Subtract
MA
WB
Division Pipeline

## Slide 50: WAR – Operand Buffer
A maybe good enough demo
DIV --, R1, --
SUB R1, --, --
Read R1
Register File
…
MA
WB
Division Pipeline
Duplicate R1/R2 here

## Slide 51: Data Hazard - WAW
Is it a fake hazard?
DIV R1, --, --
SUB R1, --, --

## Slide 52: WAW – Register Renaming
Allocate a mapping entry each time
  This is a full delegate to the register
  Further read and write will be redirected to this mapped register
rename_entry = alloc_entry()
rename[rd] = rename_entry
r1_data = data[rename[rs1]]
++use[rename[rs1]]
r2_data = data[rename[rs2]]
++use[rename[rs2]]
IF
ID
EX
MA
WB
data[rename_entry] = result
if use[rename_entry] == 0 {
dealloc(rename_entry) }

## Slide 53: WAW – Register Renaming
Program
  Algorithm
  Data structure
Architecture
  Pipeline logic
  Bookkeeping
rename_entry = alloc_entry()
rename[rd] = rename_entry
r1_data = data[rename[rs1]]
++use[rename[rs1]]
r2_data = data[rename[rs2]]
++use[rename[rs2]]
IF
ID
EX
MA
WB
data[rename_entry] = result
if use[rename_entry] == 0 {
dealloc(rename_entry) }