## Slide 1: Computer Architecture W4D2: Branch Prediction & Superscalar
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Care! Downstream modules hurt timing!
What should you do to bypass a branch result?
  Combinational?
  Sequential?
IF
ID
EX
MA
WB

## Slide 3
Chart: Simulating a “Simple” CPU
| median | multiply | qsort | rsort | towers | vvadd | gmean
ours | 1 | 1 | 1 | 1 | 1 | 1 | 1
gem5 | 1.0523 | 0.84436 | 1.0689 | 0.84962 | 1.582 | 1.0015 | 1.0418

## Slide 4: Characterization
Assumption: All the architectures discussed are pipelined.
Instead of saying Tomasulo or other algorithms, I will characterize:
  In-/out-of-order
  (Non-)Speculative
  Single/Multi-issue

## Slide 5: Roadmap
Why do we have branch predictor?
How is it achieved?

## Slide 6: Branches
Control hazard: Before executing this instruction, PC is not determined
Why is it bad?
  2-cycle bubbles
bnez t1, △
F D X M W
? ? F D X M W
bne t1, x0, △

## Slide 7: Control Hazard: Solution
Fast branch: Execute the branch in ID
  + It seems to know the result one cycle earlier
  - More complicated decoding for comparison and addition
  - Decoding sometimes takes more than you expect
bnez t1, △
Look out! This △ is a relative address!
5-stage pipeline is just 5 things to do in instruction execution.
The granularity of explanation is determined by understandability.

## Slide 8: Recap: Aligned Code Loading
12-bit encoding
[-2048, 2047]
Within an aligned page
Recap: Branch Encoding

## Slide 9
Recap: Branch Encoding
MSB the same location
  Critical for sext!
[10:5] the same location
Switch is too expensive

## Slide 10: Control Hazard: Trends
Trends to have more stages for better frequency
  486 (1989): 5
  Pentium (1993): 7
  Pentium II (1997) / III (1999): 12
  Pentium 4 (2000-2007): 22
  Nehalem (2008): 20-24
  Haswell (2013) / Skylake (2017) / Cooper lake (2020): 14-19
More stages → more stages on decoding → more delays on ctrl hazard

## Slide 11: Solution (CONT’D)
Delayed Branch: Branching takes effect one insn. Later
MIPS adopts this and regrets
  Not a big win compared to today’s CPU
  Not always finding such an instruction
bnez t1, △
addi t2, t2, 1
sub t3, t3, t4
This instruction is STILL part of last BB
This instruction is NOT

## Slide 12: (1) It’s better to be wrong once in a while than to be right all the time.
Solution - PACT’18: Keynote

## Slide 13: Impossibility of exploiting ILP: [c. 1972]
“..Therefore, we must reject the possibility of bypassing conditional jumps as being of substantial help in speeding up execution of programs.
In fact, our results seem to indicate that even very large amounts of hardware applied to programs at runtime do not generate hemibel (> 3x) improvements in execution speed.”
Riseman and Foster, IEEE Trans. Computers, 1972
Flynn bottleneck

## Slide 14: Exploiting ILP [Fisher c.1982]
Key idea:
  Branch speculation
  Backup/re-execute if prediction is wrong
  Dynamic branch prediction [Smith,Patt]
Infallibility is for popes, not parallel computing
Broader lesson:
  Runtime parallelization: essential in spite of overhead and wasted work
  Compile-time parallelization: only part of the solution to exploiting parallelism (see Itanium)

## Slide 15: Solution: Branch Prediction
Speculative Execution
Guess what to do
  Execute the instruction before the results

## Slide 16: Branch Prediction (CONT’D)
Guess what to do
Correct Speculation
  Save two bubble cycles
Incorrect Speculation
  Roll back executions.
  Execution time no penalty.
  No worse than 2 stalls
F D X M W
F D X M W
F D X M W
? ? F D X M W
F D X M W
F D X M W
F D X M W

## Slide 17: Misprediction: Recovery
Incorrect Speculation
F D X M W
F D X M W
F D X M W
F D X M W
F D - - -
F - - - -
F D X M W
X→F/D: Override with noop
X→D/X: Override with noop
X→F: Tell the right inst to fetch
Flush the incorrect instructions
Key Idea: Stop the execution before committing to states

## Slide 18: Paradox: When to predict?
More stages → more stages on decoding → more delays on ctrl hazard
  We will know it is a branch late
  We will invoke a prediction late
Proposed Solution: BTB
  Branch Target Buffer

## Slide 19: BTB: Branch Target Buffer
Buffer: It is an on-chip memory
  On-chip memory/SRAM/Cache/$
  Key difference
    Register knows value immediately
    SRAM knows value 1-cycle later
Fetcher requests from I-memory
Memory responses to Decoder
IF
ID
I$
BTB

## Slide 20: Assassyn: Dealing w/ Memory
Recap: Callback function
This is useful for memory usage
  Memory “pushes” data to the next stage
  Calls its call back function.
x = async foo(1, 2) // A Promise returned
x.when(function (result) {
// use the returned value here.
})
foo will be done, but not immediately;
a promise is returned to use the result when ready

## Slide 21: BTB: Branch Target Buffer (CONT’D)
A small cache LUT
  Key: PC address
  Value: Target PC
BTB
31:20
19:10
9:2
1:0
19:10
13:2
19:10
13:2
…

## Slide 22: BTB: Branch Target Buffer (CONT’D)
Hit? It is a branch!
No hit? It is not necessarily not a branch
31:20
19:10
9:2
1:0
19:10
13:2
19:10
13:2
…
Associativity
Pentium 4:
2k Entries
4-way associative

## Slide 23: BTB: Branch Target Buffer (CONT’D)
Aliasing?
  It’s ok… At least it does not hurt the correctness
Entry Creation: By Execution
31:20
19:10
9:2
1:0
19:10
13:2
19:10
13:2
…
Note: this target address is the branch taken

## Slide 24: BTB: Branch Target Buffer
Part I: Should I take the branch?
  Applies to conditional branches
  Predicts T/NT
  Hard
Part II: If taken, where should I go?
  For control transfers
  Predict target PC

## Slide 25: Branch Direction Prediction
Branch instructions are often “biased”
Biased: A likelihood to a specific direction
  E.g. for-loop often takes branching
BHT: Branch History Table
31:20
19:10
9:2
1:0
19:10
1: T/N/…
19:10
1: T/N/…
…
Do what I did last time!

## Slide 26: BHT can easily be messed…
Consider the code below
Actual i-branch: (T, T, N) x n
Prediction: _, (T, T, N) x n
TTNTTNTTNTTNT...
?TTNTTNTTNTTN...
for (j=0; j<n; ++j)
for (i=0; i<3; ++i)
// what ever
: Half of the correctness?

## Slide 27: 2-Bit Saturating Counters
Strong T
Weak T
Strong N
Weak N
I am confidently correct!
Hmm. I am confident again!
Did I do anything wrong?
Fine, I change my mind…
I am confidently correct!
Now, BHT entry has 4 states encoded in 2 bits.

## Slide 28: 2-Bit Saturating Counters (CONT’D)
Now BHT has 4 states encoded in 2 bits
TTNTTNTTNTTN...
TTtTTtTTtTTt...
Now we are 66.66% correct…
  Slightly better…
  Can we do even better?

## Slide 29: 2-Level Predictor: Correlated
Outcomes are correlated to its history
31:20
19:10
9:2
1:0
19:10
3: TTN
19:10
3: TTT
…
23-bit Pred
History Table
Look up
Prediction Table

## Slide 30: Design Decision 1: Global/Local BH?
Local Design: Each entry has its own history
31:20
19:10
9:2
1:0
19:10
3: TTN
19:10
3: TTT
…
23-bit Pred
Look up
Prediction Table

## Slide 31: Design Decision 1: Global/Local BH?
Global Design: Look up uses global register history
31:20
19:10
9:2
1:0
19:10
19:10
…
23-bit Pred
23-bit Pred
3: TTT
Global History Register

## Slide 32: Design Decision 2: How many bits of history?
More bits → more history → better prediction
More bits → lower utilization
  Some history never happen at all
Typically 8-12 bits of history

## Slide 33: Correlated Predictor [Yale Patt et al. 1991]
He should have taught you some basic computer arch weeks ago (but not)
Uses to be the one with the most ISCA paper until 2019 (?)
  But then his student Onur dominates

## Slide 36: Wait… Did I miss something?
Part I: Should I take the branch?
  Applies to conditional branches
  Predicts T/NT
  Hard
Part II: If taken, where should I go?
  For control transfers
  Predict target PC

## Slide 37: PC Prediction: Return Address Stack
RAS tracks the call sequence
jal pushes PC+4 onto RAS
Prediction returns the top of RAS on return

## Slide 38: Summary
Typical breakdown:
  Branch 20%, Load 20%, Store 10%, Other: 50%
  75% branches are taken
  Prediction can achieve around 95% accuracy
No penalty? Yes and no.
  Yes: No performance penalty, no worse than stalls
  No: transistors are charged
    Jpredict + [(1-%mispredict) * Jexec]

## Slide 39: Characterization
Assumption: All the architectures discussed are pipelined.
Instead of saying Tomasulo or other algorithms, I will characterize:
  In-/out-of-order
  (Non-)Speculative
  Single/Multi-issue

## Slide 40: Multi-issue/Superscalar
Before
After
F D X M W
F D X M W
F D X M W
F D X M W
F D X M W
F D X M W
A single instruction each time.
Multiple instructions each time
(Ideal case)

## Slide 41: Multi-issue/Superscalar
Before
  Single fetch
  Single decode
  Single execution
  Single MA
  Single WB
IF
ID
EX
MA
WB
IF
ID
EX
MA
WB
After
  Multi-fetch
  Multi-decode
  Multi-execution
  Multi-MA
  Multi-WB

## Slide 42: Wider…
Wider fetch: It’s OK.
Typically cache line is 256-bit
256/32=8 instructions
  Simple for RISC-like
  What if X86 does not align?
    Pad with noops
Wider decoder
  Still RISC is simple
Wider operand validity
  N2 complexity
  N-wide issue
  N-wide reg read

## Slide 43: Recap: Flattening Arrays
Dude, there is no high-dimensional arrays
int b[200][100]; // 2d array
// use array
b[i][j]
// flattened array use
((int*)b)[i*100+j];

## Slide 44: Even Worse in Hardware 🤦🏻‍♀️
Dude, there is no “arrays” in hardware
logic a[32][31:0];
logic rs[5:0];
// read a[rs];

## Slide 45: Even Worse in Hardware 🤦🏻‍♀️
Dude, there is no “arrays” in hardware
Reads are switches of selecting bits
logic a0[31:0]; logic a1[31:0]; ...
logic rs[5:0];
logic value[31:0];
if (rs == 5'0) value = a0;
else if (rs == 5'1) value = a1;
else if (rs == 5'2) value = a2;
// ...

## Slide 46: Wider… (CONT’D)
Wider execution 🤯
Say, 4-issue, it is OK to have 4 sets of integer ALUs
  Maybe? But div is expensive
Even worse, how about floating point div?
How about laning?

## Slide 47: Wider… (CONT’D)
Wider execution 🤯
How about laning?
Decoder Lane 1
rs1
rs2
rd
Decoder Lane 2
rs1
rs2
rd
…
Executor ALU 1
Executor ALU 2
…

## Slide 48: Wider… (CONT’D)
Wider execution 🤯
Wider bypassing
Decoder Lane 1
rs1
rs2
rd
Decoder Lane 2
rs1
rs2
rd
…
Executor ALU 1
Executor ALU 2
…

## Slide 49: Wider…
Wider Register Writeback
Dude, there is no “arrays” in hardware 🤦🏻‍♀️
logic a[32][31:0];
logic rd1[5:0];
logic rd2[5:0];
@always(posedge clk) begin
if (we1) a[rs1] <= some0;
if (we2) a[rd2] <= some1;
end

## Slide 50: Even Worse in Hardware 🤦🏻‍♀️
Synthesizer helps you though…
@always(posedge clk) begin
if (we1 & (rd1 == 0)) a0 <= some0;
else if (we2 & (rd2 == 0)) a0 <= some1;
if (we1 & (rd1 == 1)) a1 <= some0;
else if (we2 & (rd2 == 1)) a1 <= some1;
...
end

## Slide 51: Summary
Not only operand validity check
It is almost everything in N×M-order of cost
  Operand
  Bypassing
  Read
  Write
Routing is N×M