## Slide 1: Computer Architecture W5D2: Cache
Jian Weng
Computer Science
CEMSE, KAUST

## Slide 2: Recap: What is the slowest stage?
Motivation
  Memory access is slow.
  We want to make it faster
How?
  Understanding the concept of data hierarchy
  Then we explain what are caches
IF
ID
EX
MA
WB

## Slide 3: Amdahl’s Law (CONT’D)
Say, in a system, memory access occupies 60%, while computation occupies 10%.
  What if we make the computation 1 million × faster?
    Execution Time:
  What if we halve the memory access time, what do we get?
The original execution time w/ optimized part excluded
Optimized execution time
Execution Time:
Speedup:

## Slide 4: Motivation
Compute is fast!
Look at this CPU, whose clock rate is 4.3GHz
An addition can be done within ~0.23ns

## Slide 5: Motivation
Memory is slow in latency: A memory access takes nearly 50-100ns, which is 200-400x slower
(General) Memory Unobtainable Goal
Affordable
Big to fit all the data
Fast in access

## Slide 6: The Memory Wall
Compute grows 1.3-1.5x yearly
Memory? 7%

## Slide 7: The Memory Wall
The trend is still true today

## Slide 8: Storage Hierarchies
Type | Latency | Throughput | Size
Register | 0 | / | ~KB
SRAM | ~1-10ns | ~5TB/s | ~100MB
Memory | ~100ns | ~100GB-3TB/s | ~32GB-2T
Disk | ~1ms | ~0.5GB/s | ~2T-100T
Typically smaller sizes for larger bandwidth and latency

## Slide 9: How does cache benefit?
Capture memory accesses’ locality
Temporal Locality
  Memory accessed within a brief time period will be frequently accessed again
Spatial Locality
  Memory near the memory accessed will be frequently access again
👉🏻 True for both data and instruction
  I$ & D$

## Slide 10: What does cache do?
Read/write the data does not just bring the data from the memory
  Also bring the whole block into a cache
  Next time, read from cache to save time when accessing again
This saves traffic from memory
  What is traffic?
CPU
L1
Mem

## Slide 11: How does cache benefit? (CONT’D)
Recap what we had in speculative execution
  Penalty: Cannot worse than bubbles
  Benefit: Execute instruction early
What about cache?
  Care! We do have penalties on mis
  %mis * (latcache + latmem) + %hit * latcache

## Slide 12: Cache Architecture
We focus on private L1 cache first
We focus on L2 read today
  Write later
Caches are transparent
Caches are hidden!
GPU scratchpad are reconfigurable
  48KB=16KB+32KB
  Scratchpad: sw managed
  Cache: hw managed
Core 0
L1
L2
Core 1
L1
L2
LLC shared across cores
Private L1
GPU-SM
L1

## Slide 15: More on Storages
Static Random Access Memory (SRAM)
  6 transistors per bit (depends)
  Optimized for speed and less optimized for density
  Fast: Speed and energy saving proportional to area
  Mixes well with compute logics
Dynamic RAM (DRAM)
  1 transistor and 1 capacitor per bit
  Optimized for density
  Slow (>40ns for internal access and >100ns for pin-to-pin)
  Hard to integrate with logics

## Slide 16: More on Storages (CONT’D)
DRAM
  DRAM read is destructive
  A memory read destructs the data in memory
  Read data will be broadcast to both response and write back to retain the data
    Which is another key reason DRAM is slower
Both DRAM and SRAM are volatile
  Disks are non-volatile
  So called NVM, non-volatile memory

## Slide 17: IP Blackbox
SRAM blackbox from ASAP lib

## Slide 18: IP Blackbox
Key difference: SRAM has 1-cycle latency w/ fixed data width, 33-bit
Why 33? Maybe for valid

## Slide 19: Question: What if I want wider data access?
A cache line is 256-bit, how?
Combine more of these blackbox blocks and concatenate them.
This is called interleaving.
Bank 0
Bank 1
Bank 2
Bank 7
…
0
1
2
7
…
0
1
2
7

## Slide 20: Question: How are these banks connected?
H-tree
  A recursive topology to minimize the wire length
  Each node looks like a H

## Slide 21: A Basic Cache Structure
Cache: An array of blocks
  Each block/cacheline is 32-byte/32B
  A 32KB cache has in total 1024 blocks
To find the block
  How?
  Slice the address
Tag[31:15]
Index[14:5]
Offset[4:0]

## Slide 22: A Basic Cache Structure (CONT’D)
Slice the address
Offset
  Each block is 32-byte, 2(4-0)+1=32
Index
  In total 1024 blocks, 2(14-5)+1=1024
Tag
  31-15+1=16 bits
Tag[31:15]
Index[14:5]
Offset[4:0]

## Slide 23: Indexing a Cache Entry
Consider a simplest case 1-way associative
Addressable Cache w/ 1024 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&

## Slide 24: Indexing a Cache Entry
Just like read an array from an array 🤦🏻‍♀️
Addressable Cache w/ 1024 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&

## Slide 25: Indexing a Cache Entry
The array entry can be broken down into 3 fields
Addressable Cache w/ 1024 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&

## Slide 26: Indexing a Cache Entry
The array entry can be broken down into 3 fields
Addressable Cache w/ 1024 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&

## Slide 27: Wait… Isn’t Tag and Valid Bit overhead?
Yes.
In total: 32B + 1-bit valid + 16-bit tag = 273
Overhead: 17 + 1 = 18
Overhead(%): 18 / 273 ≈ 6.6%
Quiz: What is the overhead of having 48-bit address?

## Slide 28: Associativity
Associativity: Say, 4 way. OK, four duplications of this.
Addressable Cache w/ 1024 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&
x4

## Slide 29: Associativity
Associativity
  Say, 4 way. OK, four duplications of this.
  Even more associativity? More on this later.
    It badly hurts the latency
Read out 4 entries in //
Additional logics:
  Select the one matches: If no one matches, miss!
  Select the one to kick out when associativity is full

## Slide 30: Hill’s 3C Miss Rate of Caches
Compulsory
  1st time of access
Capacity
  Missed caused by capacity
  I will give you an example later (your homework)
Conflict
  Caused by finite associativity
  I will also give you an example later

## Slide 31: Cache Size
Increasing cache size always helps
  Correct non-sense
But with diminish returns
  Cache buffering is in the granularity of working sets

## Slide 32: What is working set?
An example of matrix multiplication
If you do a naïve matrix multiplication, the working set is 3N2, A, B, and C
A
B
C
=

## Slide 33: Can we have a better working set?
Linear algebra taught us we can block-ize the matrix multiplication
Say, we have a block, 32×32
A
B
C
=
C0,0
B0,0
B1,0
A0,0
A0,1

## Slide 34: Temporally and Spatially Local
Say, we have a block, 32×32
When accumulating the submatrix C0,0, we have a working set of 3×(32×32) for each K
A
B
C
=
C0,0
B0,0
B1,0
A0,0
A0,1

## Slide 35: Temporally and Spatially Local
Say, we have a block, 32×32=1024
32×32×4B = 4kB, 3 matrices = 12kB
Hopefully, it fits in a local L1
A
B
C
=
C0,0
B0,0
B1,0
A0,0
A0,1

## Slide 36: From a Traffic View
The bigger block, the more reuse as I discussed before
Say, n2 size of block, we have 3n2 of work set
  3n2 traffic from DRAM to L1: Less favor but inevitable
  n3 traffic from L1 to core: More favored trying to maximize
A
B
C
=
C0,0
B0,0
B1,0
A0,0
A0,1

## Slide 37: We are not done yet!
Look at these blocks in a fine-grain view.
B is still accessed in column major
Transpose B in each submatrix
A
B
C
=
C0,0
A0,0
A0,1
B0,0
B1,0

## Slide 38: Homework: Optimize a GeMM
I believe you do not need to do SIMD, the compiler will transform it for you.
Just make a good scope of working sets.
Maybe I should as TA for an online judge.
Say, we do a 20483 with O3 enabled for 0.5s time limit

## Slide 39: Block Size
Bigger block
  More conflicts: Fewer entries
  Fewer first access miss
  May increase the latency when missing
  Fewer bits on indexing, more bits on offset
  Tag unchanged
  Fewer entries & Tag unchanged: Lower overhead
Tag[31:15]
Index[14:5]
Offset[4:0]

## Slide 40: Block Size (CONT’D)
Block size
Bigger blocks for better continuous or adjacent access
  For worse scattering accesses
  For more conflicts
A good block size is 32-128B
  Program-dependent
Block Size
Miss Rate

## Slide 41: Conflict (w5d1/transpose.c)
To my surprise, I can still replicate this on an laptop produced in 2023
Transpose an 1024x1024 array
  100%
Transpose an 1023x1023 array
  -2047: -2 less works
Transpose an 1025x1025 array
  2049: 2% more works
How much execution time differences will we have?

## Slide 42: Conflict (CONT’D)
N=1024, i*N+j is too perfect aligned with cache way associativity, which causes associativity conflict to frequently kick out and bring in values.
What should we do?

## Slide 43: Way-Skewed Cache
Each way we can use a different function to allocate different entries of cache
Cache Assoc. Way 1
Index[14:5]
Skew Function 1
Cache Assoc. Way 2
Index[14:5]
Skew Function 2
Cache Assoc. Way 3
Index[14:5]
Skew Function 3

## Slide 44: Overwhelming Conflicts
When having too many blocks mapping to a same way, what should we do?
Kick out.
Kick out who?
  Furthest used in the future
  Dude, there is no magic in this world

## Slide 45: Overwhelming Conflicts
Some realistic options
  FIFO
  Least recently used
    A good heuristic for temporal locality
  Not most recently used
    Remember the index of most recently used
    Kick anyone but this one
  Not recently used
    Randomly clear the associate bit
    Set this bit when used

## Slide 46: Fully Associative Caches
We CANNOT do this  for the cost reason
Addressable Cache w/ 1 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&
x1024

## Slide 47: Fully Associative Caches (CONT’D)
A built-in comparator in near memory
=
Addr [31:5]
=
Addr [31:5]
=
Addr [31:5]
=
Addr [31:5]
…
Request
Data
Data
Data
Data
…
Still, we cannot do 1024-way assoc.
Luckily, in most cases we do not need it.

## Slide 48
This is still expensive
Addressable Cache w/ 1024 Entries
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&
x4
Design Decision: Separate Tags and Data

## Slide 49: Separate Tags and Data (CONT’D)
This is still expensive
Addressable Cache w/ 1024 Tags
Tag[31:15]
Index[14:5]
Offset[4:0]
Tag in Cache [31:15]
=
Data in Cache 32-Bytes
Valid
&
x4

## Slide 50: Separate Tags and Data (CONT’D)
Only 4x logics for tags, and this is slightly more complicated
Addressable Cache w/ Data
Index[14:5]
Offset[4:0]
Data in Cache 32-Bytes
Tag Valid?
Way

## Slide 51: Separate Tags and Data (CONT’D)
This introduces one more stage. Can we do best of both? 1 access of data, and separated t/d?
Addressable Cache w/ Data
Index[14:5]
Offset[4:0]
Data in Cache 32-Bytes
Tag Valid?
Way

## Slide 52: Separate Tags and Data (CONT’D)
Yes. Everything can be speculative 🤦🏻‍♀️
Addressable Cache w/ Data
Index[14:5]
Offset[4:0]
Data in Cache 32-Bytes
Tag Valid?
Way
Predictor

## Slide 53: Limitations of Cache
Dude, magic helps, to some extent
Recap this: A memory access takes nearly 50-100ns, which is 200-400x slower
  Caches can mitigate this 200-400 cycles of bubbles
But there is no magic in this world
Recap this also: A 7B LLM is 53GB, while a GPU HBM is 2T, so 2T/53GB<40.
  We cannot synthesize more than 40 tokens/s.
Do they contradict? Or how do they work together?